## Slide 1: Maintenance Weekly
TileCal Op Meeting, 20 January 2022
Irakli Minashvili, Chris Thomas, Dawit Belayneh, Katie Hughes

## Slide 2: Cooling Status
LBC 33
  Identified leak using air hoses
  Drawer opened Jan 19
  Leak location on the HV side inside of drawer, we bypassed this segment and saw huge improvement in PPV cycle
  Drawer closed, current temperature is acceptable

## Slide 3: Cooling Status
Loop 16
  Seemed as though there were leaks in many different modules according to air hose tests with the water circulation OFF
  Circulation turned back ON today and problems resolved (?)
  We will not touch this loop any further
Loop 13
  Leak identified in this loop with air hoses
  Currently locked (?)