## Slide 1: CIS Tech Update
Chicago Meeting, August 15th, 2022
Peter Camporeale and Jacky Li

## Slide 2
CIS Constant Updates
  June 23 - July 14
  July 15 – August 9
Low Voltage Power Supply / Detector Control System Monitoring
L1 Trigger System
Fast Calo Simulation
Test Beam
ATLAS Control Room Shifts
Life
Outline

## Slide 3
Transition from last generation of Katie and Dawit to Peter and Jacky
1.a. CIS Constant Update: June 23-July 14

## Slide 4
Independently done by Peter and Jacky
1.b. CIS Constant Update: July 14 – August 8

## Slide 5
Use known input charge to calibrate ADC counts of front-end electronics
  3-in-1 cards contain 5,100 pF capacitors
  Input known charge 60 times, sample each pulse 7 times  pulse amplitude
  Fit mean pulse amplitude (in ADC counts) to injected charge
CIS calibration runs are taken between ATLAS runs, roughly 3 times per week
Use TUCS to analyze data for recent runs and identify DQ issues in channels
  Monitor individual channels: drifting, high scatter, half-gain?
  Monitor overall performance: percent change, long-term stability, RMS/mean
  Upload new constants to database
Summary of CIS

## Slide 6
Overview:
  Monitoring the current supplied to 5V motherboards in Tile modules
  Currently, there is an online database. We want to collect this data to monitor current trips and integrate it with current systems
  DDV applies “smoothing” to DCS: it only updates if the current change is outside a given interval
2. LVPS/DCS Monitoring
Online DDV data/plotting

## Slide 7
Done:
  Connected with Felipe Martins
  Generated code for accessing/checking DCS values
  Became familiar with some legacy code
  Added new functionalities: time-averaging of current
To do:
  Integrate the code into TIO (online monitoring system)
  Connect with Sergei Chekalev
2. LVPS/DCS Monitoring

## Slide 8
3. L1 Calo Trigger System
Connected with Danijela Bogavac
Overview of system:
  Towers are collections of PMTs and front-end electronics that sum events covering to produce trigger signals
Goals:
  Monitoring of trigger rates in the L1 Calo
  Integrate with Data Quality Monitoring Display (DQMD) in ACR
  Analyze PMT scans to identify low trigger rates
Schematic of L1 calo tower

## Slide 9
Done:
  Reviewing code/documentation
  Tour of ACR to see these systems in action
To do:
  Meeting with Danijela again next week to commence project
3. L1 Calo Trigger System
Current L1 Calo Mapping Tool in Online Histogram Presenter (OHP)
Current L1 Calo Mapping Tool Data Quality Monitoring Display (DQMD)

## Slide 10
Dawit explained his code and the goal of the simulations
Done:
Recreated plots
To do:
None, until further notice.
4. Fast Calo Simulation (FCS)

## Slide 11
Meeting with Irakli Minashvili
Done:
  Checked the legacy Tile system in Test Beam.
  Fixed Mobidick HV problem
To do:
  Shift training before new test beam in November
  None maintenance until further notice (Irakli is taking his vacation)
5. Test Beam

## Slide 12
Peter’s first shifts were August 2 – August 8
  Monitoring data quality for Tile modules
  Reporting on LAr status and major problems
  More shifts in late August and September
Jacky’s shift training is in late August, will take shifts next semester
6. ATLAS Control Room Shifts

## Slide 13
Old CIS techs leaving
  Katie left on July 25
  Dawit left on August 13
Prof. David Miller’s visit late June
Getting settled in the city
Learning/refreshing driving manual
7. Life
June 29th , Dinner at Luigi’s

## Slide 14
Jacky teaching Peter to drive manual
7. Life (More Pictures)
Peter playing the carillon at Cathedrale St.-Pierre
At Bains de Pâquis

## Slide 15
Add questions here if we have any
8. Questions

## Slide 16
Thank you for your attention 